G8 Homework – C19 : Forces

1.	The diagram below shows a system of 5 strings and a beam of mass 1 kg holding a 2 kg mass. What are the tensions T1 and T2 in the two strings shown? (take g = 10 m/s2)									[2]

2.	Many automobile passengers suffer neck injuries when their stationary car without head rests is hit by a car from behind. Explain this phenomenon using Newton’s first law.								[2]

3.	If Mr. Chris were chasing Tina, his enormous mass would be very threatening. But if Tina zigzagged, Mr. Chris’s mass would be to her advantage. Why? (Hint: inertia.)									[2]

4.	A high-flying jet cruises at an altitude of 30 000 feet at a constant velocity of 700 km/h. The force of thrust of the jet engines is 40 000 N. How much air friction acts on the craft? Explain.							[2]

5.	A stationary trolley of mass 1 kg is free to move along a frictionless horizontal surface. For the first 10 s, a steady horizontal force of 0.5 N is applied to the trolley.

a)   What is the acceleration of the trolley?					[1]

b)   What is the speed of the trolley after 10 s?				[2]

c)   For the next 20 s, the applied force is removed. What happens to the acceleration of the trolley? What happens to the speed of the trolley?	[2]

6.	When a rocket of mass 3 tons (1 metric ton = 1000 kg) lifts off with a force of Fl = 50 000 N, the rocket experiences air resistance of approximately 5000 N. What is the acceleration of the rocket? [take g = 10 m/s2]				[2]

7.	The figure below shows a block of mass 4 kg resting on a table. A force of 5 N is applied to the block pulling it to the right, which gives it a constant acceleration of 1 m/s2.

a)	What is the resultant force acting on the block?			[2]

b)	Explain why the resultant force is less than the applied force.	[1]

c)	If the applied force acts on the block for 5 s, what will the speed of the

block be after 5 s?							[2]

d)	After 5 s, the applied force is removed. What will the new acceleration be?

[2]

8.	A lift is moving upwards at a constant acceleration of 2 m/s2. Given that the lift has a mass of 500 kg, what is the tension in the cable? [take g = 10 m/s2]	[2]

9.	Using Newton’s law of Universal Gravitation, explain why g, the acceleration due to gravity is a constant.							[2]

10.	How does the force of gravity between 2 bodies change when the distance between them is doubled?							[2]

11.	Using Newton’s 3rd law, explain how a squid moves.			[2]

12.	Explain why a person in a car pushing on the steering wheel will not be able to make the car move forward.							[2]