Magnetic Fields Practice Worksheet

Part 1:  Draw an arrow in the "compass" circles to designate the direction of the magnetic field at those locations near the permanent magnets:

1.							2.

3.

Part 2:  Draw an arrow (or dot, or X) in the "compass" circles to designate the direction of the magnetic field at those locations near these moving charges and current-carrying wires (use right hand rule #1).  Let circles with a dot in them represent direction out of the page and circles with an X in them represent direction into the page:

4.			5.  			6.			7.

8. 						9.

10.  Current in a wire moves from the back window to the front white board.  A compass is place underneath the wire on the floor, which way will it point?

11.  Current in a wire moves from the floor to the ceiling in the middle of the class.  A compass is placed near the overhead screen, which way will it point?

Part 3:  State the direction of the magnetic FORCE on these moving charges or current-carrying wires when near these external magnetic fields (use right hand rule #2) .  Circles with a dot in them represent directions out of the page and circles with an X in them represent directions into the page.  B is the letter that designates magnetic field:

12.			13.  			14.				15.

16.  		17.

18.  Protons move from the Big Periodic table to the overhead screen while the floor of the room is a North Pole of a magnet.  Which way are the protons forced to move?

19.  Current in a wire moves from the ceiling to the floor while the white board is the South Pole of a magnet.  Which way does the wire move?

20.  Electrons move from the white board to the back window while the overhead screen is a South Pole of a magnet.  Which way are the electrons forced to move?

# Text boxes

Current into the page

e-